## Slide 1
Robot deployment framework for cleaning services
A customer job becomes declared sub-tasks, decisions over the team's evidenced capabilities, and a conditional job plan
Layer 1
Customer job
and requirements
Declared work requirement: 3 rooms, 3 whiteboards with a marked region, 2 glass partitions, 3 wall spots, 1 supply request.
Sub-task requests: capability, domain, context and target, allowed modes, accepted evidence levels, exact settings, owner-authorised force range, metric bounds, required human roles, inputs from other sub-tasks, logical slot.
Layer 2
Team capability
register
Human interaction (UR3 cell)
Command, confirmation and stop by gesture; object handover.
Visual targeting (UR5 cell)
Attended detection of a marked target region that selects cleaning waypoints.
Controlled contact (G1 humanoid)
Force-regulated wiping with a final hold, after a confirmation.
Capability profiles: evidence level, domain and provenance, exact settings, metrics, qualifiers, source pins.
Human capabilities (team)
Declared roles (operator, confirmer, attendant), training and availability.
Live facts at decision time: shared safety, area access, location safety and contact permission, input, visibility, path, availability.
Layer 3
Assignment and
operating decisions
Layer 3a: per-sub-task decision
Over the register: SELECT, CONFIRM, ASK, WAIT, WITHHOLD or REFUSE, with every option's reasons.
Optimised allocation, scheduling and fleet sizing from measured durations and costs.
Layer 3b: conditional job plan
Robot and setting per sub-task, required human roles and actions, open owner choices, pending confirmations, waits, and blocked sub-tasks with the missing evidence named.
Layer 4
Execution and
feedback
Dispatch through platform adapters after owner approval.
Execution under each case's own gates.
Outcome records added to the register for later jobs.
Executed in a deployment case
Implemented offline
Proposed
Illustrative job: one floor
corridor
blue: glass partitions
red: marked regions and spots
wall spots